## Slide 1: Introduction to Arduino Microcontroller
Prepared by:
Md. Asaduzzaman
Dept of ICT, MBSTU

## Slide 2: Contents
What is Microcontroller?
What is Arduino?
Types of Arduino?
Installation process
Types Sensors? - Digital, Analog sensors.
Motor control
Coding structure and examples with C/C++ Library File? 1. Data types and operators. 2. What is “Function”? 3. Control statements [if, if… else, switch case.]. 4. Loop statements[while, for, do… while.]. 5. Common functions.

## Slide 3
What is a Microcontroller ?

## Slide 4: Microcontroller
It is a micro-computer. As any computer it has internal CPU, RAM,IOs interface.
Microcontroller = internally (CPU+RAM+IO interface) integrated device
It is used for control purposes, and for data analysis.
Must Need a Programmer.
Work as, both Master or Slave device.
Famous microcontroller manufacturers are MicroChip, Atmel,Atmega, Intel,IBM etc.

## Slide 5: Microcontroller Programmer
Hardware :
PIC Programmer, Pocket AVR Programmer etc.
Software : (AVR,AVRISP,USBISP,USBASP) .
USB PIC Microcontroller Programmer

## Slide 6
What is the difference between Microcomputer and Microcontroller ?

## Slide 7: What is Arduino Microcontroller ??
It is Open Source (Hardware + Software) and single board microcontroller.
Work as, both Master or Slave device.
Arduino = internally CPU+RAM+IO interfaces + programmer (AVR,AVRISP,USBISP,USBASP) .
In 2005, a project was initiated to make a device for controlling student-built interactive design projects that was less expensive than other prototyping systems available at the time.
Founders Massimo Banzi and David Cuartielles named the project after Arduin of Ivrea and began producing boards in a small factory located in Ivrea.

## Slide 8: General Structure of Arduino ?

## Slide 9: Arduino Specification
Microcontroller ATmega328
Operating Voltage 5V and 3.3 V
Baud Rate : 9600, 14400, 19200, 28800, 38400, 57600, or 115200 bps.
Input Voltage (recommended) 7-12V
Input Voltage (limits) 6-20V
Digital I/O Pins 14 (of which 6 provide PWM output)
Analog Input Pins 6
DC Current per I/O Pin 40 mA
DC Current for 3.3V Pin50 mA
Flash Memory 32 KB (ATmega328) of which 0.5 KB used by Bootloader
SRAM 2 KB (ATmega328)
EEPROM 1 KB (ATmega328)
Clock Speed 16 MHz
Other Prototyping Platform:
Raspberry pie
Beagle board
Panda board
Cotton candy
Cubie Board
APC Rock
Hackberry
Gooseberry

## Slide 10: Types of Arduino ?

## Slide 11: Specification of different Types of Arduino -01

## Slide 12: Specification of different Types of Arduino -02

## Slide 13
Arduino Based Sensor

## Slide 14: Types of Sensor
Two types:
Digital Sensor
Analog Sensor

## Slide 15: Frequently Used Sensor
Humidity sensor (DHT22) - Digital Sensor
Temperature sensor (LM35) - Analog Sensor
Water detector sensor (Simple Water Trigger) - Digital Sensor
PIR SENSOR - Digital Sensor
ULTRASONIC SENSOR - Digital Sensor
Sound Sensor - Digital Sensor
GPS

## Slide 16: Humidity Sensor (DHT22) –Digital Sensor
Technical Details
Power − 3-5V
Max Current − 2.5mA
Humidity − 0-100%, 2-5% accuracy
Temperature − 40 to 80°C, ±0.5°C accuracy

## Slide 17: Temperature Sensor (LM35) Analog Sensor
Technical Specifications:
Calibrated directly in Celsius (Centigrade)
Linear + 10-mV/°C scale factor.0.5°C ensured accuracy (at 25°C)
Rated for full −55°C to 150°C range
Suitable for remote applications

## Slide 18: Water Sensor (Digital Sensor)
Technical Specification:
Water sensor has three terminals –
S,Vout(+), and GND (-).
Connect the sensor as follows −
Connect the +Vs to +5v on your Arduino board.
Connect S to digital pin number 8 on Arduino board.
Connect GND with GND on Arduino.

## Slide 19: PIR (Pyroelectric/Passive Infrared Radiation) Sensor (Digital Sensor)
Technical Specification:
PIR sensor has three terminals : Vcc, OUT and GND.
Connect the sensor as follows −
Connect the +Vcc to +5v on Arduino board.
Connect OUT to digital pin on Arduino board.
Connect GND with GND on Arduino.

## Slide 20: Ultrasonic Sensor (HC-SR04) - Digital Sensor
Technical Specifications
Power Supply − +5V DC
Quiescent Current − <2mA
Working Current − 15mA
Effectual Angle − <15°
Ranging Distance − 2cm – 400 cm/1″ – 13ft
Resolution − 0.3 cm
Measuring Angle − 30 degree
Connect the +5V pin to +5v on your Arduino board.
Connect Trigger to digital pin 7 on your Arduino board.
Connect Echo to digital pin 6 on your Arduino board.
Connect GND with GND on Arduino.

## Slide 21: Sound Detection Sensor (Digital Sensor)

## Slide 22
Control the different type of motor with Arduino

## Slide 23: Types of Motor ??
There are three different type of motors −
DC motor
Servo motor
Stepper motor
DC Motor
Servo motor
Stepper motor

## Slide 24: Necessary Things to done a Project with Motor
Motor Driver : To control the direction of the spin of DC motor, without interchanging the leads, you can use a circuit called an H-Bridge(Motor Driver). An H-bridge is an electronic circuit that can drive the motor in both directions.
Example : L298, L293 ,ESC etc.
L298 Motor Driver

## Slide 25: Arduino Installation
First you must have your Arduino board and a USB cable.
Download Arduino IDE and driver.
IDE Link: ARDUINO 1.8.5 : https://www.arduino.cc/en/Main/Software
(go for windows installer) Download and Install it.
Driver Link: https://www.dropbox.com/s/a1d4837hbfylipb/windows-driver-installer.exe?dl=0 Download and Install it.

## Slide 26: Run on IDE

## Slide 27: Basic Structure of a Sketch
Open/Create a Sketch and Save it with .ino extension.

## Slide 28: Open an Example Sketch

## Slide 29: Select a Board

## Slide 30: Select a Communication port

## Slide 31: Upload a Sketch
A - used to check compile error.
B - Upload the program (Sketch).
C - Create new Sketch.
D - Open a Sketch.
E - Save a Sketch.
F – Serial monitor is Used to Visualize of transformation of serial data.

## Slide 32
Arduino Programming with C/C++ Library File

## Slide 33: Life Cycle of Arduino Sketch

## Slide 34: Input and Output Function
pinMode(Pin_no, Mode);
Mode= Input/Output on Analog or Digital pin
digitalRead(D_Pin_no);
digitalWrite(D_Pin_no, High/Low);
delay(time_ms);
other functions:
analogRead(A_Pin_no);
analogWrite(A_pin_no, PWM_input); //PWM.

## Slide 35: PWM (Pulse Width Modulation)

## Slide 36: Data Type : Like as C/C++

## Slide 37: Operators : Like as C/C++
- Math operators: [+,-,*,/,%,^,++]
- Logic operators: [==, !=, &&, || ]
- Comparison operators: [==, >, <, !=, <=, >=]
Compound Operators: ++ (increment) -- (decrement) += (compound addition) -= (compound subtraction) *= (compound multiplication) /= (compound division)
- Other : ; = Semicolon, {} = curly braces, // = single line comment,
/*Multi-line comments*/

## Slide 38: Control Statement: Like as C/C++
If(condition) {…………}
If(condition) {………….} else {…………..}
If (condition) {…} else if (condition) {….} else {………}
switch (var) { case 1: //do something when var equals 1 break; case 2: //do something when var equals 2 break; default: // if nothing else matches, do the default // default is optional }

## Slide 39: Loop Statement: Like as C/C++
Do… while: do { Statements;
break;
}
while(condition); // the statements are run at least once.
While: While(condition) {statements; break; }
for for (int i=0; i <= val; i++){ statements;
break; }

## Slide 40: Basic Structure of a Simple Project: 01 Blinking LED (Send a Digital Serial Write command to a Slave (Sensors, LEDs, Motors etc.))
void setup() //the setup function runs once when you press reset or power the board.
{
pinMode(3, OUTPUT); // initialize digital pin 3 as an output.
}
void loop() // the loop function runs over and over again forever.
{
digitalWrite(3, HIGH); // turn the LED on (HIGH is the voltage level).
delay(1000); // wait for a second.
digitalWrite(3, LOW); // turn the LED off by making the voltage LOW.
delay(1000); // wait for a second.
}

## Slide 41: Circuit Diagram of Project: 01

## Slide 42: Basic Structure of a Simple Project: 02 Digital Serial Data Reading (Receive a command from a Slave (Sensors, LEDs, Motors etc.))
int pushButton = 2; // digital pin 2 has a pushbutton attached to it. Give it a name:
void setup()
{
Serial.begin(9600); // initialize serial communication at 9600 bits per second:
pinMode(pushButton, INPUT); // make the pushbutton's pin an input:
}
void loop()
{
int buttonState = digitalRead(pushButton); // read the input pin:
Serial.println(buttonState); // print out the state of the button:
delay(1); // delay in between reads for stability
}

## Slide 43: Basic Structure of a Simple Project: 03 Analog Serial Data Reading (Receive a command from a Slave ((Sensors, LEDs, Motors etc.))
void setup()
{
Serial.begin(9600); // initialize serial communication at 9600 bits per second:
}
void loop()
{
int sensorValue = analogRead(A0); // read the input on analog pin 0:
float voltage = sensorValue*(5.0/1023.0);
// Convert the analog reading(0-1023) to a voltage(0-5V):
Serial.println(voltage); // print out the value you read:
}

## Slide 44: Circuit diagram of Project- 03
Potentiometer

## Slide 45: Basic Structure of a Simple Project: 04 (Send a Analog Serial Write PWM command to a Slave (Sensors, LEDs, Motors etc.))
void setup()
{
Serial.begin(9600); // initialize serial communication at 9600 bits per second:
}
void loop()
{
int Value = random(0,1023);
//set a analog serial data (which goes from 0 - 1023) to a voltage (0 - 5V):
float voltage = Value * (5.0 / 1023.0);
analogWrite(A1,voltage); // write the input on analog pin 1:
Serial.println(voltage); // print out the value you write:
}

## Slide 46
Can anyone tell us the Sketch (code) of merging the idea of Project -01,02,03 and Project -04 ??

## Slide 47: Merge circuit Diagram of Project -03 and Project -04

## Slide 48: Test Our Skills : (PWM) Anyone Please explain Where PWM is used?
int led = 3,brightness = 0,fadeAmount = 5;
void setup()
{
pinMode(led, OUTPUT);
}
void loop()
{
analogWrite(led, brightness);
brightness = brightness + fadeAmount;
if (brightness == 0 || brightness == 255)
{
fadeAmount = -fadeAmount ;
}
delay(30);
}

## Slide 49: Basic Project -05 Control the Spin of Motor
const int pwm = 10 ;
const int in_1 = 9 ;
const int in_2 = 8 ;
void setup()
{
pinMode(pwm,OUTPUT) ;
pinMode(in_1,OUTPUT) ;
pinMode(in_2,OUTPUT) ;
}
void loop()
{
digitalWrite(in_1,HIGH) ;
digitalWrite(in_2,LOW) ;
analogWrite(pwm,255) ; //Clockwise for 3 secs
delay(3000) ;
digitalWrite(in_1,LOW) ;
digitalWrite(in_2,HIGH) ;
delay(3000) ; //Anti-Clockwise for 3 secs
}

## Slide 50: Basic Project -05 Control the Spin of Motor Circuit diagram

## Slide 51: Project -06 : A Simple Home Security System
Basic Idea : To build an human detection System for your Home using Arduino on 220v AC.
Instruments:
Arduino
PIR Sensor.
Relay Module (The relay board works on 220V AC .So keep necessary safety measurements.).
LED and Buzzer.
Motor.
Jumper Wire and Breadboard.
L298 Motor Driver.

## Slide 52: Project -06 :Smart home Security Circuit Diagram

## Slide 53: Project-06: Sketch of Home Security System
int LED = 3;
int PIR = 2;
int Buzzer = 7;
void setup()
{
pinMode(LED, OUTPUT);
pinMode(Buzzer, OUTPUT);
pinMode(PIR, INPUT);
}
void loop() {
int value = digitalRead(PIR);
if (value == HIGH){
digitalWrite(LED, HIGH);
digitalWrite(Buzzer, HIGH);
}
else {
digitalWrite(LED, LOW);
digitalWrite(Buzzer, LOW);
}
}

## Slide 54: Project -07:Clap controlled Smart home Circuit Diagram

## Slide 55: Video Tutorial of Building the Clap Control

## Slide 56: Project References
http://www.instructables.com/technology/arduino/ for project idea.
https://playground.arduino.cc/Projects/Ideas .
https://codebender.cc/home for project code Must need Firefox/chrome.
https://github.com for project code.
https://youtube.com for tutorial.
https://learn.sparkfun.com/tutorials for tutorial.
https://www.allaboutcircuits.com/projects/category/arduino/ for tutorial.
https://diyhacking.com/diy-projects/arduino-projects/ for project idea.
http://mertarduinotutorial.blogspot.com for tutorial.
Arduino for Dummies by- John Nussey.
Arduino Programming by- Simon Monk.

## Slide 57
Any Question ??

## Slide 58
Thank You